## Slide 1: New Rules! Morphing with The New ADA Standards An Overview
Don Brandon
Director
Northwest ADA Center

## Slide 2: Northwest ADA Center – Region X
Located in Mountlake Terrace with CCER (Center for Continuing Education in Rehabilitation)
Program in Rehabilitation Medicine at the University of Washington
Funded by NIDRR (National Institute on Disability and Rehabilitation Research)

## Slide 3: The National Network of ADA Centers
Funded By NIDRR
Common Research
National Programs
Mandated By TITLE V of The ADA
Same 800-949-4232
National Web Site www.adata.org

## Slide 4: What Do We Do?
We Provide Comprehensive And Accurate Information On ADA Compliance, Including:
  Employment Of Persons With Disabilities (E.G., Reasonable Accommodation)
  Accessibility In Facilities, Programs And Information (Public And Private)
  Assistive Technology, Universal Design

## Slide 5: Why We Can Be Valuable To You!
We Are Knowledgeable Professionals Providing Information About The ADA
We Are Not An Enforcement Authority
We Are Not Lawyers Or Advocates
Note: All Contacts Are Confidential

## Slide 6: Ways We Can Help
Technical Assistance
Training
Information Dissemination
Research
Public Awareness

## Slide 7: New Rules !
Employment
  New Interpretation of Definition of Disability
  Mitigating Measures No Longer Applicable
  Clarity on Types of Conditions Covered
Programs & Services
  Web Sites
  Ticketing
  Service Animals
Facilities
  Signs, Parking,
  Two Standards (1991 2010) & Safe Harbors

## Slide 8: Agenda
How The 2010 ADA Standards Developed
The Regulations That Are a Part AS 2010
The Basics Are the Same (CAT)
The Technical Stuff!
Scoping More Prescriptive More Areas Are Defined
Chapter Variables

## Slide 9: Civil Rights Standards & Facilities
1991 Standard
UFAS or ADAAG
Revised 1994
Added 1998,2002 & 2004 Chap 11-14
2010 Standard
Safe Harbor 3/15/2012
ADAAG
Notes: Civil Rights standards effect facilities creating minimum requirements. The ADAAG has had 3 significant enfroceble Standards, m41991, 1994, & 2010

## Slide 10: The Basics: DOJ Adopts 2004 ADAAG & Adds Provisions
Access Board’s Guidelines Become Standards For New Construction And Alterations
DOJ Adds
  Triggers And Applicability
    Compliance Date
  Scope
    Fixed Or Built-in Elements On A Site
    Figures, Notes Do Not Establish Enforceable Requirements
  Structural Impracticability
  Path Of Travel Details
  Noncomplying New Construction And Alterations

## Slide 11: ANSI A117 Is 50 Years Old This Month

## Slide 12: Revisions to ADA regulations published September 15, 2010
President Announced, And DOJ Posted, Final ADA Regulations On July 26, 2010
Published In Federal Register September 15, 2010
First Major Updates/Revisions In 19 Years
Two Regulations
  Title II: State And Local Governments (Title II), 28 CFR Part 35
  Title III: Public Accommodations And Commercial Facilities, 28 CFR Part 36
Regulations, Appendices, Standards Are At DOJ’s ADA Web Site (Www.Ada.Gov).

## Slide 13: Harmonization
ICC/ANSI A117.1-2003 IBC 2003

## Slide 14: ADA/ABA Accessibility Guidelines - 2004

## Slide 15: New Format
Numbering System
New Figures (Informational Only)
All Dimensions In Text
(Not Just Figures)
New Advisory Notes Follow Provision

## Slide 16: ADA-ABA Guidelines,

## Slide 17: At Last!
New ADA Standards

## Slide 18: ADA 2010 Standards Has 3 Parts Applicable to Title II & III
Technical
Chapters
(Part III)
ADA Scoping
(Part II)
28 CFR Part 36 Subpart D

## Slide 19: Additional Requirements Applicable to Specific Types of Facilities
Applies To New Construction And Alterations, Program Access, And Barrier Removal.
Final Rules Describe Additional Requirements Beyond Those Originally Contained In The ADA/ABA Accessibility Guidelines.

## Slide 20: http://www.ada.gov/regs2010/2010ADAStandards/2010ADAstandards.htm

## Slide 21: Challenges
Learning The New Standards
Figuring Out What To Do In The Next Six Months
Understanding The “Safe Harbors”
(New Concept)
Modifying Certain Types Of Policies
Keeping Up With Other Regulatory Developments
Notes: An hour glass with some of the sand in the bottom, most in the top.

## Slide 22: Triggering Events
Title II
  Start Of Physical Construction Or Alterations, 35.151(c)
Title III Tied To Permits, If Granted, 46.406(a)
  If State/Local/County Government Requires Permits, Date That Last Application For Building Permit Or Permit Extension Certified Complete
  If Government Doesn’t Certify Completion Of Applications, Then Date Of Last Application For Permit Or Extension
  If Government Doesn’t Require Permits, Start Of Physical Construction Or Alterations

## Slide 23: Definition of “Existing Facility”
Rules Add A Definition Of “Existing Facility”
An “Existing Facility” Is “A Facility In Existence On Any Given Date, Without Regard To Whether The Facility May Also Be Considered Newly Constructed Or Altered Under This Part.”
Notes: Give examples

## Slide 24: Title II – Compliance
For Program Access, Until Compliance Date, Covered Entities May Choose To Use Either The UFAS, The 1991 Standards, Or The 2010 Standards

## Slide 25: Title III Compliance – Existing Facilities Before Compliance Date
Requirement: Elements That Do Not Comply With The Corresponding Requirements For Those Elements In The 1991 Standards, Must Be Modified To The Extent Readily Achievable.
(Barrier Removal) (Section 36.304)
Applicable Standard Before Compliance Date (18 Months After Publication In The Federal Register):
  1991 Standards; Or
  2010 Standards (Section 36.304(d)(2)(ii)(a)

## Slide 26
1991
UFAS
2010
Title II Can Choose Any of the Standards Till 3-15-12
Title III Can Only
Choose Two Till 3-15-11 (Safe Harbor Option)
Notes: 26

## Slide 27: Maintenance of Accessible Features (New Provision)
If The 2010 Standards Reduce The Technical Requirements Or The Number Of Required Accessible Elements Below The Number Required By The 1991 Standards, The Covered Entity May Reduce The Level Of Accessibility In Accordance With The 2010 Standards.
Stadium Seating
Notes: Give examples.

## Slide 28: Maintenance
Maintenance Of Accessible Features:
Not In “Standards” Sections
Sections 35.133(c) And 36.211 (C) Of General Requirements:
If The Standards Reduce The Technical Or Scoping Requirements For An Element Below What The 1991 Standards Required, The Technical Or Scoping Standards May Be Reduced Per 2010 Standards.
Example: 1991 Standards Require 4% Of Seats To Have Ald’s In Auditorium. 2010 Require Only 2%. You Can Reduce Existing Number To 2%.
Notes: Red flag icon in heading

## Slide 29: Additional DOJ Requirements
Social Service Center Establishments
Housing At Places Of Education
Assembly Areas
Medical Care Facilities
Residential Dwelling Units
Detention And Correctional Facilities
Places Of Lodging

## Slide 30: Social Service Center Establishments
Facilities With More Than 50 Beds With Common‐use Bathing Facilities Must Provide At Least One Roll‐in Shower With A Seat.
If Common‐use Shower Facilities For Both Genders Are Provided, Roll‐in Showers Required For Each Group.

## Slide 31: Social Service Center Establishments
Section 35.151(e) and Section 36.406(d)
Social Service Establishments Are Required To Comply With The Requirements For Residential Facilities, Including, But Not Limited To The Provisions In Sections 233 And 809.
In Sleeping Rooms With More Than 25 Beds, A Minimum Of 5 Percent Of The Beds Must Have Clear Floor Space.

## Slide 32: Housing at a Place of Education
“Housing Operated By Or On Behalf Of An Elementary, Secondary, Undergraduate, Or Postgraduate School, Or Other Place Of Education, Including Dormitories, Suites, Apartments, Or Other Places Of Residence.”
Defined At Section 35.104 And Section 36.104

## Slide 33: Housing at a Place of Education
Section 35.151(f) and Section 36. 406(e)
Kitchens Within Housing Units Containing
Accessible Sleeping Rooms With Mobility
Features Or On Floors Containing Accessible
Sleeping Rooms With Mobility Features Must
Provide Turning Spaces & Accessible Route That Comply With The Requirements Of A.S. 2010

## Slide 34: Housing at a Place of Education
Multi‐bedroom Housing Units That Contain
Accessible Sleeping Rooms With Mobility
Features Must Have An Accessible Route
Throughout The Unit In Accordance With The
Requirements Of The Residential Dwelling
Units Standards.

## Slide 35: Housing at a Place of Education
Apartments Or Townhome Facilities Which Are
Leased On A Year‐round Basis Exclusively To
Graduate Students Or Faculty, And That Do Not
Contain Any Public Or Common Areas Available
For Educational Programming, Are Required To
Comply With The Requirements For Residential
Facilities.

## Slide 36: Assembly Areas
Section 36.151(g) And Section 36.406(f)
The 2010 Standards Require:
Dispersion Of Wheelchair Spaces
And Companion Seats To All Levels That Include Seating Served By An Accessible Route In
Stadiums, Arenas, And Grandstands.

## Slide 37: Assembly Areas
Wheelchair Spaces And Companion Seats Are Required To Be Horizontally Dispersed Have Seating Encircling, In Whole Or In Part, A Field Of Play Or Performance Area.
Wheelchair Spaces And Companion Seats May Not Be Located On Temporary Platforms Or Other Moveable Structures Except In Certain Specified Circumstances.
Wheelchair Spaces And Companion Seats Shall Be Placed To Assure Line‐of Sight

## Slide 38: Assembly Areas
Wheelchair Spaces And Companion Seats Are Required In Each Specialty Area That Provides Spectators With Distinct Services Or Amenities That Are Generally Not Available To Other Spectators. (Section 36.308)
This Requirement Is Included In, Rather Than In Addition To, Wheelchair Space Requirements Set Forth In Table 221.2.1.1 In The 2010 Standards.

## Slide 39: Medical Care Facilities
Section 35.151(h) And Section 36.406(g)
The AS 2010 Require: Dispersion Of
Accessible Patient
Bedrooms In A Manner
That Is Proportionate By
Type Of Medical
Specialty.

## Slide 40: Title II—Residential Dwelling Units
Standards Require At Least 5 Percent To Be Accessible To Persons With Mobility Disabilities And At Least 2 Percent To Be Accessible To Persons With Communication Disabilities.
Section 35.151(j) Applies These Requirements To Those Housing Programs Operated By Public Entities That Provide Units For Sale To Individuals.

## Slide 41: Title II—Residential Dwelling Units
Residential Units Subject To The Section
504 Regulations Of The Department Of Housing And Urban Development (HUD) Defer To The HUD Regulations For The Scoping Requirements.

## Slide 42: Title II ‐ Detention and Correctional Facilities ‐ Section 35.151(k))
Increases Required Scoping For New Construction And Alterations Of Accessible Cells To 3 Percent, But No Fewer Than One.
Cells With Mobility Features Shall Be Provided In Each Classification Level.

## Slide 43: Places of Lodging (Section 36.406(c))
Places Of Lodging Include Other Facilities Such As Timeshare And Condominium Properties That Operate Similarly To Hotels. (Defined At Section 36.104)
These Facilities Must Comply With Transient Lodging Requirements.

## Slide 44: Places of Lodging
May Combine Multiple Facilities On A Single Site That Have 50 Or Fewer Guest Rooms And Are Constructed Or Altered Subject To The Same Permit Application.
More Than 50 Guest Rooms Treated Separately

## Slide 45: Places of Lodging
Rule Exempts From The Alterations Requirements, Guest Rooms That Are:
1) Not Owned Or Substantially Controlled By The Entity That Owns, Leases, Or Operates The Overall Facility; And
2) Where The Physical Features Of Guest Room Interiors Are Controlled By The Individual Owners.

## Slide 46: Places of Lodging That Are Part of Mixed Use Facilities
Mixed‐use Facilities ‐ Where A Facility Contains
Both Residential Dwelling Units And Other
Units Designed As Transient Lodging Facilities,
The Residential Dwelling Units Are Not Covered
By The Transient Lodging Standards.
Section 36.406 (C)(3)

## Slide 47: Current ADA Standards
Transit Facilities
(e.g., bus stops/stations, rail stations):
DOT’s ADA standards (2006)

## Slide 48: Element-by-Element Safe Harbor: Existing Facilities
Elements That Comply With The Corresponding Requirements For Those Elements In The 1991 Standards Do Not Need To Be Modified To Meet The 2010 Standards Unless Those Elements Are Altered On Or After March 15, 2012.
Safe Harbor Does Not Apply To Those Elements In Existing Facilities That Are Not Subject To Specific Requirements In The 1991 Standards.

## Slide 49
ADAAG 2010 Standard
Can Use Lower Applicable Standard
After 3-15-2012; 2010 Standard Only
Can Use Either Standard Till 3-15-2012
Safe Harbor
Only Applicable Element By Element
Title II Entities Can Use 1991 or 2010 or UFAS
Exist & Complies with 1991 Standard, No Change Ever Required; Except for Alteration after 3-15-2012

## Slide 50: Elements in 2010 Standards Not Subject to Safe Harbor
Residential Facilities And Dwelling Units
Amusement Rides
Recreational Boating Facilities
Exercise Machines And Equipment
Fishing Piers And Platforms
Golf Facilities
Miniature Golf Facilities

## Slide 51: Elements in 2010 Standards Not Subject to Safe Harbor
Play Areas
Saunas And Steam Rooms
Swimming Pools, Wading Pools, Spas
Shooting Facilities With Firing Positions,
Miscellaneous
  Team Or Player Seating
  Accessible Route To Bowling Lanes
  Accessible Route In Court Sports Facilities

## Slide 52: Path of Travel - Safe Harbor
Both Title II And Title III Specify That If A Covered Entity Has Constructed Or Altered Required Elements Of A Path Of Travel In Compliance With The Applicable Standards (1991 Or UFAS), Before March 15, 2012, They Are Not Required To Retrofit Such Elements To Reflect Incremental Changes In The 2010 Standards, Just Because They Alter A Primary Function Area Served By The Path Of Travel.

## Slide 53: …Title II and III alterations: Safe Harbor
Alterations Don’t Trigger Requirement To Alter Elements Of Path Of Travel That Already Comply With The 1991 Standards.
Title II: 35.151(b)(4)(ii)(c)
Title III: 36.403(a)(1)
Notes: Graphic of safe harbor: lighthouse by shore

## Slide 54: Existing facilities: safe harbor
Program Accessibility (Title II)
Basic Requirement Stays:
  Every Program Must Be Accessible When Viewed In Its Entirety
  Whether Something Is “Accessible” Is Measured By Reference To Standards
The “Measure”/Reference Point Changes (1991, 2010)

## Slide 55: …Existing facilities: safe harbor
New “Safe Harbor”: Elements Complying With UFAS Or 1991 Standards Don’t Have To Be Altered Just For Sake Of Program Access Even After March 2012
  Areas Not Addressed In 1991 But Addressed In 2010 Are Not Subject To Safe Harbor: Recreation, Play Areas, Etc.
Barrier Removal (Title III): Similar Safe Harbor

## Slide 56: Using The Safe Harbor Before 3-25-12
Document Existing Elements Complying With 1991 Standards (Or UFAS If Title II)
If Changes Are Required, Remove Barriers To Program Access (Or Title III Barriers) Under 1991 Or 2010 Standard Considering Safe Harbor

## Slide 57: Resources
Regulations, Appendices, Standards Are Available At Doj’s ADA Web Site At www.AdA.Gov
For Answers To Specific Questions, DOJ Toll-free Ada Information Line:
800-514-0301 (Voice)
800-514-0383 (TTY)
Network Of Ada Centers (Formerly Known As DBTAC”S)
800-949-4232 (Voice/Tty)
U.S. Access Board Web Site At Www.Access-board.Gov.

## Slide 58: Alterations: title II
“Path Of Travel” Requirement Now Applies Under Title II Too. 35.151(b)(2) And (4).
  Aka 20% Rule: If You Alter A “Primary Function Area,” You Have To Comply With Alterations Standards For That Space, Plus Spend Up To 20%
  On Path Of Travel Accessibility
  (Route To Space, Restrooms,
  Drinking Fountains, Phones)
Structural Impracticability

## Slide 59: ABA Standards
(Federal facilities)
Similar Standards In Effect For All Federally Funded Facilities (Except Housing)
Housing – UFAA Still Applies (HUD To Update Standards)

## Slide 60: AS 2010 The Technical Stuff!

## Slide 61: CHAPTER 1
Dimensions – Range Instead Of Absolute Dimension Where Possible
Construction And Manufacturing Tolerances
Scoping Percentages/Ratios (Round Up)
Referenced Standards

## Slide 62: 2010 ADA Standards
104 Conventions
104.1 Dimensions
Dimensions That Are Not Stated As A
Maximum Or Minimum Are Absolute.
104.1.1 Construction And Manufacturing Tolerances
All Dimensions Are Subject To Conventional Industry Tolerances Except Where The Requirement Is Stated As A Range With Specific Minimum And Maximum End Points.

## Slide 63: Ranges instead of absolute dimensions
Water Closet Centerline (16-18”)
Width Of Ambulatory Accessible Stall (35”- 37”)

## Slide 64: Some Absolute Dimensions Remain
E.G. Transfer Shower Stall (36” X 36”)
(Measured To Center Points; Manufacturing Tolerances Recognized)

## Slide 65: Tolerances do not apply to ranges

## Slide 66: CHAPTER 2
General Scoping
New Construction
Exceptions
Additions and Alterations

## Slide 67: New Construction
All areas must comply except:
  Exempted structures/ spaces
  Work areas (ADA facilities)
  Partially scoped spaces

## Slide 68: New Construction
Example: Medical Care Suite
Mechanical (exempt)
Clustered toilet rooms (partial scoping – 50%)
Work areas (partial access) – e.g, reception area, nurses station

## Slide 69: General Exceptions
Construction Sites
Raised Areas (Security, Life/Fire Safety)
Spaces Accessed By Ladders, Catwalks, Crawl Spaces, Narrow Passageways
Machinery Spaces

## Slide 70: General Exceptions
Single Occupant Structures (E.G., Toll Booths)
Accessed Only By Below-grade Passageways Or Elevated Above Standard Curb Height

## Slide 71: General Exceptions
Recreation Facilities
Raised Structures Used Solely For Refereeing, Judging, Or Scoring A Sport
Raised Boxing/ Wrestling Rings
Water Slides And Raised Diving Boards/ Platforms
Animal Containment Areas Not Open To The Public

## Slide 72: Work Areas
Accessible Circulation Paths
Exceptions:
Areas < 1000 Sq. Ft.
Paths = Integral Part Of Equipment
Exterior Areas Fully Exposed To Weather

## Slide 73: Work Areas
Exempt:
Areas Under 300 S.F. That Are Elevated At Least 7” As An Essential Functional Condition Of The Space (Excluding Raised Courtroom Stations)

## Slide 74: Alterations
Standards Apply Based On:
Planned Scope Of Work
Technical Feasibility
Primary Function Areas/ Path Of Travel

## Slide 75: CHAPTER 3
Building Blocks:
Floor/ Ground Surfaces
Changes in Level
Turning Space
Clear Floor Space
Knee & Toe Clearance
Protruding Objects
Reach Ranges and Operable Parts

## Slide 76: Reach Ranges
Side reach range reduced:
48” – 15”
(same as forward reach)

## Slide 77
Permitted overlap clarified (objects with required knee/ toe clearance)
Turning Space

## Slide 78
Overlap limited to 1 arm of T-shaped space
(2 arms unobstructed for approach, backing up)
Turning Space

## Slide 79
Knee/Toe Clearances
Specified in Chapter 3 for all elements (e.g., lavs, sinks, counters, tables, etc.)
Depth: 17” – 25”

## Slide 80
Knee/Toe Clearances
Knee Clearance:
Height: 27”min.
Depth: 8” min.

## Slide 81
Knee/Toe Clearances
Beyond 8” depth: clearance can reduce to 9” min. at 11” depth
(6:1 slope)

## Slide 82
Knee/Toe Clearances
Toe Clearance:
Height: 9” min.
Depth: 6” max. (of usable CFS)

## Slide 84: CHAPTER 4
Accessible Routes:
Walking Surfaces
Doors And Gates
Ramps And Curb Ramps
Elevators
Platform Lifts

## Slide 85: Accessible Routes
At Least One Accessible Route To Building Entrances From:
Streets And Sidewalks
Transportation Stops
Parking
Passenger Loading Zones
(Where Provided)

## Slide 86: Accessible Route Scoping
Section 206

## Slide 87: Accessible Routes
Clarifications:
if circulation path interior, AR must be interior
AR not req’d if no pedestrian route provided
AR not req’d to mezzanines in buildings without elevators

## Slide 88
Exceptions (206.2.3)
AR between floors (“elevator exception”)
Private sector facilities only:
less than 3 stories OR less than 3,000 sf/ flr)

## Slide 89
Exceptions (206.2.3)
Exception not allowed for:
Shopping centers/ malls
Professional offices of health care providers
Terminal, depots, or stations used for public transportation

## Slide 90
Exceptions (206.2.3)
New Exception For Public (Gov’t) Buildings:
2 Story Only And
1 Floor Has: No Public Space AND Max.
Occupancy Of 5
E.G. Train Dispatch
Or Boat Traffic Towers

## Slide 91
Exceptions (206.2.3)
Additional exceptions:
detention and correctional facilities
residential facilities
transient lodging (certain
(multi-story units)
air traffic control tower cab
qualified historic facilities

## Slide 92: Doors and Gates
Recess: greater than 8”
(forward approach clearance flush with plane of door)

## Slide 93: Doors and Gates
Other changes:
hardware height (34” – 48”)
limited projections into clear width
closing speed
smooth surface (push side)
vision lights

## Slide 94: Ramps
Slope: 1:12 Max.
Cross Slope: 1:48 Max.
Clear Width: 36” Min.
Rise: 30” Max.
Level Landings
Handrails (Both Sides)
Edge Protection

## Slide 95: Ramps
Edge Protection
◄Barrier (rail or curb)
Extended Platform►

## Slide 96: Handrails
Ramps, Stairs, And Walkways
Knuckle Clearance: 1 ½” Min. (Not Absolute)
Diameter: 1 ¼” – 2” (Instead Of 1 ½” Max.)
Applies To Outer Diameter (Clarification)
Circular & Noncircular Cross Sections

## Slide 97: Handrails
Handrails must comply where provided along walkways

## Slide 98: Curb Ramps
Landing 36” min. required at the top

## Slide 99
Curb Ramps
Lack of space at top makes curb ramps difficult to use

## Slide 100: Curb Ramps
Detectable Warnings – required at:
Transit facilities (DOT standards)
FHWY funded projects
Other public sidewalks (strongly recommended)
- Board to address in new ROW guidelines

## Slide 101: Curb Ramps
DWs – revised specifications available where provided (draft ROW guidelines)

## Slide 102: Detectable Warnings
www.access-board.gov/adaag/dws/update.htm

## Slide 103: Elevators
Standard Elevators
Destination-Oriented Elevators
Existing Elevators (alterations)
Limited Use/ Limited Application Elevators (LULAs)
Private Residence Elevators

## Slide 104: Standard Elevators
Car sizes – more alternatives
designs providing turning space within car recognized

## Slide 105: CHAPTER 5
General Site & Building Elements
Parking
Passenger Loading Zones
Stairways
Handrails

## Slide 106: Parking
Clarifications:
Scoping Calculated Lot-by-lot
Exempt: Parking For Buses, Trucks, Delivery And Law Enforcement Vehicles, Impound
Marking Of Access Aisles
Sign Height (60” Min.)
Angled Vans Spaces (Aisle On Passenger Side)

## Slide 107: Parking
Van Spaces: 1 of 6 accessible spaces
(instead of 1:8)

## Slide 108: Parking (208)

## Slide 109: Passenger Loading Zones
At least 1 for every 100 linear ft. of loading zone space provided

## Slide 110: Passenger Loading Zones
Aisles - Same Level As Pull-up Space
Aisles To Be Marked
No Level Changes In Space Or Aisle

## Slide 111: Stairways
Covered: all stairs that are part of means of egress
(exceptions for altered and assembly stairs)
• Removed: level 12” h-rail
extension at bottom
• Riser height (4”-7”)

## Slide 112: CHAPTER 6
Plumbing Elements & Facilities:
Drinking Fountains
Toilet & Bathing Rooms
Water Closets, Toilet Compartments, Urinals
Lavatories & Sinks
Bathtubs & Shower Compartments
Washing Machines & Clothes Dryers
Saunas & Steam Rooms

## Slide 113: Drinking Fountains
Where Provided At Exterior Site Or Floor, 2 Units Required (Wheelchair & Standing Access)
  Alternative: Single “Hi-lo” Unit Multiple Installations: 50% Of Each Type (Can Round Up Or Down)

## Slide 114: Clustered Toilet Rooms
50% Scoping For Single User Toilet Rooms Clustered At One Location That Serve Same Users

## Slide 115: Private Toilet Rooms
“Adaptability” Permitted:
Private Use
Single Occupant
Accessed Only Through Private Office

## Slide 116: Private Toilet Rooms
Clarified That Adaptability Allows:
Later Provision Of Grab Bars (Reinforcement/ Blocking)
Alternative Toilet Seat & Lavatory Heights
Removable Base Cabinetry At Lavs
Door Swing Into Fixture Clearances (Where Swing Can Be Reversed)

## Slide 117: Water Closet Clearance
Lavatory overlap no longer permitted

## Slide 118: Water Closets
Original ADAAG (fig. 28) permitted overlap

## Slide 119: Toilet Rooms
Range for toilet centerline
lavatory cannot overlap toilet clearance (except in dwelling units)

## Slide 120: Toilet Rooms
Allows space for side transfers

## Slide 121: Toilet Rooms
fixtures can be recessed
shorter (24” min.) rear grab bar allowed in this case

## Slide 122: Toilet Rooms
Door man. clearance; swing outside fixture clearances

## Slide 123: Toilet Rooms
Doors Can Swing Into Fixture Clearances If Clear Floor Space (30” X 48” Min.) Provided Outside Swing

## Slide 124: Turning Space
60” Diameter Circle Or “T” Turn (Elements With Knee/Toe Clearance Can Overlap)
T-turn: Overlap Limited To One Segment

## Slide 125: Toilet Rooms
Turning Space Can Overlap Fixture & Door Clearances; Door Can Swing Into Turning Space

## Slide 126: Toilet Rooms
Same Requirements Apply For Any Design/ Configuration
(Turning Space Not Shown)

## Slide 127: Toilet Rooms
… Including Less Common Designs
(Turning Space Not Shown)

## Slide 128
Clearances:
1 ½” Behind (Abolute)
1 ½” Min. Below
12” Min. Above (New)
Grab Bars
Other Changes:
2” Max. Diameter (Instead Of 1 ½”)
Circular And Non-circular Cross Sections

## Slide 129: Grab Bars
Clearances At Grab Bars Help Ensure Usability

## Slide 130: Grab Bars
ANSI A117.1 requires 18” min. vertical grab bar (ADA and ABA guidelines do not)

## Slide 131: TP Dispenser
Dispenser location

## Slide 132: TP Dispenser
grab bar height (33”-36”) and clearances further limit location of non-recessed dispensers

## Slide 133: Children’s Toilets
Alternate Specifications Permitted For Toilets Designed For Children 12 & Younger

## Slide 134: Children’s Toilets
Advisory information provides guidance according to age group
 | Ages 3 & 4 | Ages 5 - 8 | Ages 9 - 12
WC Centerline | 12” | 12” – 15” | 15” – 18”
Seat Height | 11” – 12” | 12” – 15” | 15” – 17”
Grab Bar Height | 18” – 20” | 20” – 25” | 25” – 27”
Dispenser Height | 14” | 14” – 17” | 17” – 19”

## Slide 135: Lavatories and Sinks
Apron Clearance (29” Min.) Removed
Parallel Approach - Kitchen Sinks In Spaces Without Cook Tops/ Ranges
Removable Cabinetry:
Allowed In Dwelling Units
(If Certain Conditions Met)

## Slide 136: Lavatories
Locate controls & dispensers above, not beyond, usable CFS to be within reach

## Slide 137: Lavatories
Tip: Avoid Hospital Style Lavs With Deep Projections
They Take Up More Space And Require A Greater Reach To Faucet Controls And Dispensers

## Slide 138: Sinks
Public/ Common Use: Full Access To 5%
  Classrooms
  Research Laboratory (If Used For Instruction)
  Break Room*
  Preschool Classroom*
  * Side Approach Access Allowed
Work Areas: Access Not Required (Recommended)
  Commercial Laboratory
  Research Laboratory (Employee Use Only)
  Restaurant Kitchen
  Janitor’s Sink (Exempt)
Dwelling Units: Adaptability Allowed
  Kitchens

## Slide 139: Toilet Stalls
Standard Stall

## Slide 140: Toilet Stalls
Stalls With More Than 1 Plumbing Fixture Treated As Toilet Room
Second Accessible Lav Required Outside Stall

## Slide 141: Ambulatory Stall
Where 6 Or More Stalls Provided
Parallel Grab Bars
Width: 35” – 37”
Depth: 60” Min.
Doors: Out-swinging, Self-closing

## Slide 142: Bathing Facilities
At Least One Shower Or Tub Required
Options:
Transfer Shower Stall
Roll-in Shower
Combination Transfer/Roll-in Shower (Required In Some Transient Lodging Rooms)
Tubs

## Slide 143: Transfer Stall
Clear Floor Space Positioned For Alignment With Seat

## Slide 144: Roll-in Shower (no seat)
Shower Head And Controls Permitted On Any Wall If No Seat Provided

## Slide 145: Roll-in Shower (with seat)
Shower Head/Controls Required On Back Wall Within Reach From Seat

## Slide 146: Roll-in Shower (with seat)
Improper Location Makes Controls And Shower Spray Unit Unusable From Seat

## Slide 147: Alternate Roll-in/Transfer
Location Of Controls And Shower Head On Side Or Back Wall

## Slide 148: Roll-in Showers
½” Max. Beveled Curb Allowed (New)
Other Ways To Control Water:
2% Max. Slope Allowed
Consider Trench Drain
Resource From The
Center For Universal Design
Www.Design.Ncsu.Edu

## Slide 149: Shower Spray Unit
Hand-held Shower Spray Unit Required (Exception For “Unmonitored” Facilities)
On/Off Control
Water Temperature
(120 Degrees Max.)

## Slide 150: Bath Tubs
Permanent Seat
Removable Seat

## Slide 151: Washing Machines & Dryers
1 Accessible Where 3 Or Fewer Provided
2 Accessible Where More Than 3 Provided

## Slide 152: CHAPTER 7
Communication Elements & Features:
Fire Alarm Systems
Signs
Telephones
Detectable Warnings
Assistive Listening Systems
ATMs & Fare Machines
Two-Way Communication Systems

## Slide 153: Fire Alarms
NFPA 72
(1999 or 2002)
guidelines require
110 dB max.

## Slide 154: Fire Alarms
NFPA 72 covers:
flash rate & pulse duration
location - wall & ceiling
minimum intensity
larger coverage thru fewer appliances
many spaces (other than corridors) can be covered by 1 appliance
synchronization of multiple appliances

## Slide 155: Signs
Tactile/ visual – labels for permanent rooms & spaces, exit doors
Visual only – directional or informational signs
Exempt: temporary signs, building menus, directories, addresses, company names and logos

## Slide 156: Tactile Signs
Scoping (interior & exterior):
Restroom labels (at entry)
Room numbers/ names (not likely to change)
Floor levels
Exit access/discharge
Areas of Rescue Assistance

## Slide 157: Tactile Signs
Cane detection of doorways

## Slide 158: Signs
Tactile & Visual Visual Only
“Room 123” “Exit →”
“Restroom” “Accounting Department”
“Mechanical Room” “Visitors must sign in”
“Exit”
“Floor B” Exempt
“Ballroom A” building directory
“C. Smith Room” “Mr. C. Smith, Accountant”

## Slide 159: Signs
Exempt
(temporary)
Visual
(Informational)
Tactile (Room number)

## Slide 160: Tactile Signs
Raised characters
Grade 2 Braille
Visual access (finish and contrast)
Pictograms (designating room/space)

## Slide 161: Signs
Raised Characters
sans serif
character proportion, height, spacing
line spacing
height (48” – 60”)
placement at doors

## Slide 162: Pictograms

## Slide 163: Visual Signs
“conventional form”
character proportion & spacing
character height based on viewing distance
location (40” min. height)
stroke thickness
line spacing
finish & contrast

## Slide 164: Character Style
New standards specify “conventional form”
Prohibited:
Italic Oblique script
highly decorative
or other unusual forms

## Slide 165: CHAPTER 8
Special Rooms, Spaces & Elements:
Assembly areas
Dressing, fitting, and locker rooms
Kitchens and kitchenettes
Medical care and long-term care
Transient lodging
Prison cells
Courtrooms
Dwelling units
Transportation facilities
Storage

## Slide 166: Dwelling Units
New section:
5% wheelchair accessible
2% communication access features
Recognize coverage by HUD 504 regulations

## Slide 167: Transient Lodging
Bed scoping (5%)
Communication features no longer required in all mobility access rooms (at least 1, no more than 10%)
All rooms: 32” min. clear width for doors
Housing at Places of Education (DOJ Regs)

## Slide 168: Transient vs. Residential
Transient Lodging: primarily short-term in nature/ not used as a residence
Residential: Intended to be used as a residence, primarily long-term in nature.

## Slide 169: Detention/ Correction Facilities
Accessible cells: 3% (DOJ regs)
Dispersion (DOJ regs)
Special holding cells: 1 of each type)

## Slide 170: Courtrooms
jury boxes
witness stands
judges’ benches
clerk stations
spectator areas
assistive listening systems

## Slide 171: CHAPTER 9
Built-In Elements:
Dining & Work Surfaces
Benches
Check-Out Aisles
Service Counters

## Slide 172: Sales and Service Counters
36” max. height (accessible portion)
Applies to full depth of counter
36” min. length (30” min. forward approach)
security glazing – method to facilitate voice communication

## Slide 173: Benches
Back support - new specifications

## Slide 174: CHAPTER 10
Recreation Facilities:
Amusement Rides
Recreational Boating Facilities
Exercise Machines
Fishing Piers And Platforms
Golf Facilities
Miniature Golf Facilities
Play Areas
Swimming Pools, Wading Pools, And Spas

## Slide 175: Swimming pools
Means of access:
Small (< 300 linear ft)
lift or sloped entry
Large (300 or more linear ft)
lift or sloped entry AND
transfer wall/system, stairs, lift, or sloped entry (must be different)

## Slide 176: Swimming pools
Sloped Entry
Extend to 24” – 30” below water level
1:12 maximum slope
Handrails – 33” – 38” max clear width

## Slide 177: Swimming pools
Lifts
Unassisted operation
Location (48” max water level)
Submerged depth: 18” min.
Footrests

## Slide 178: Swimming pools
Transfer Wall
Transfer System
Pool Stairs